## Slide 1
Harmonic Analysis and Distortion in HVDC Systems
Authors: Mohammed Aamir Imran
Affiliation: Power Grid Coorporation of India Limited
by MD AAMIR IMRAN

## Slide 2
Motivation and Overview
Market Growth
Global HVDC market reached $8.7B in 2023, rising fast.
Renewable Integration
Vital for connecting remote renewables like offshore wind farms reaching 110 GW EU target by 2030.
Power Quality
Harmonics threaten grid stability by causing losses and equipment faults.
Topics Covered
Generation, impact, standards like IEEE 519, and mitigation strategies.

## Slide 3
HVDC System Basics
LCC Converters
High power, cost effective. Example: Three Gorges-Changzhou ±800 kV, 7.2 GW.
VSC Converters
Offers better control, smaller footprint. Example: INELFE France-Spain ±320 kV, 2 GW.
Applications
Grid interconnections
Offshore wind integration
Back-to-back links
Case Study
DolWin3 connects offshore wind to German grid, cutting losses by 60%.

## Slide 4
Harmonics and Distortion Metrics
Harmonics Defined
Frequency multiples of 60 Hz causing distortion in the waveform.
Non-Sinusoidal Waveforms
Produced by converter switching, leading to harmonic creation.
6-Pulse Converter
Generates 6n±1 harmonics such as 5th, 7th, 11th, 13th orders.
Total Harmonic Distortion (THD)
Harmonic voltage/current ratio to fundamental. Limits: 5% (voltage), 8% (current).

## Slide 5
Harmonic Generation in HVDC
LCC Sources
Harmonics arise mainly from AC/DC switching actions.
1
VSC Sources
Harmonics linked to PWM switching above 2 kHz frequency.
2
Harmonic Spectra
12-pulse LCC and MMC-HVDC systems show differing harmonic patterns.
3
Filtering Needs
LCC requires more extensive filters than VSC due to harmonic profiles.
4

## Slide 6
Impact of Harmonics on Grid
Equipment Overheating
Transformers and motors suffer thermal stress from harmonics.
Resonance Risks
Harmonics amplify at specific frequencies causing instability.
Protection Malfunction
False relay trips and misoperation due to distorted signals.
Communication Noise
Power line communication suffers interference from harmonics.
Capacitor bank failures increase by 20% due to harmonic stress.

## Slide 7
Harmonic Standards and Mitigation
IEEE 519 Limits
Defines maximum voltage/current distortion at point of common coupling.
Passive Filters
Simple LC filters tuned to common harmonics like 5th and 7th.
Active Filters
Adaptive compensation yielding up to 98% harmonic reduction.
STATCOM Solution
Used in HVDC-VSC for dynamic harmonic mitigation and voltage support.

## Slide 8
Summary and Conclusion
Importance
HVDC is vital but introduces harmonic challenges in grids.
Analysis Need
Accurate harmonic study ensures grid stability and equipment safety.
Mitigation
Standards compliance achieved via filters and active compensation.
Future Trends
Wide-bandgap devices improve quality and reduce filter sizes by 40%.